SECTION 05 52 13, 07 72 00

ALUMINUM GUARD RAIL SYSTEM

- GENERAL

  - SECTION INCLUDES

    - Aluminum Guard Rail Systems.

  - RELATED SECTIONS

    - Section 05 12 00 - Structural Steel Framing:  Roof structure and opening support.

    - Section 05 55 00 - Metal Stair Treads and Nosings:  Miscellaneous metal supports.

    - Section 06 10 00 - Rough Carpentry:  Roof framing and opening support.

    - Section 07 42 00 - Wall Panels:  Roof curb flashing.

  - REFERENCES

    - OSHA 1910.28:  Duty to have fall protection and falling object protection.

    - OSHA 1910.29:  Fall protection systems and falling object protection-criteria and practices.

  - SUBMITTALS

    - Submit under provisions of Section 01300.

    - Manufacturer's data sheets on each product to be used, including:

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

    - Shop Drawings for Aluminum Guard Rail System:

      - Plan and section of aluminum guard rail system installation.

      - Indicate rough opening dimensions for ceiling, roof openings, and/or roof hatch size.

  - DELIVERY, STORAGE, AND HANDLING

    - Store aluminum guard rail system until installation inside under cover in manufacturer's unopened packaging. If stored outside, store under a tarp or suitable cover.

  - WARRANTY

    - Limited Warranty: Five years against defective material and workmanship, covering parts only. Defective parts, as deemed by the manufacturer, will be replaced at no charge, freight excluded, upon inspection at manufacturer's plant.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: Precision Ladders, LLC, which is located at: P. O. Box 2279; Morristown, TN 37816-2279; Toll Free Tel: 800-225-7814; Tel: 423-586-2265; Fax: 423-586-2091; Web: www.PrecisionLadders.com

    - Requests for substitutions will be considered in accordance with provisions of Section 01600.

  - ALUMINUM GUARD RAIL SYSTEM

    - Aluminum Guard Rail System and Components: Vertical and horizontal rails, mounting brackets, self-closing gate, hardware, and finishes.

      - Models:  Model AGRS-H**** [****= opening size in feet and inches; for example AGRS-H2630 is AGRS-H 2’6” x 3’0” (762 mm x 914 mm)] for a roof hatch mounted aluminum guard rail system or AGRS-F**** [****= opening size in feet and inches; for example AGRS-F2630 is AGRS-F 2’6” x 3’0”(762 mm x 914 mm)] for a floor mounted aluminum guard rail system.  Aluminum Guard Rail System as manufactured by Precision Ladders, LLC.

      - Capacity:  System shall support a load of 200 lbs applied in any direction.

      - Performance Standard:  Unit shall comply with OSHA 1910.28 and OSHA 1910.29.

    - Components:

      - Vertical and horizontal rails: Aluminum (6005-T5) 1-1/4” (32 mm) schedule 40 pipe with 1-5/8” (42 mm)OD.

      - Brackets:

        - Roof Hatch Application: Y style 5” x 1-1/4” x 1/8” (127 mm by 32 mm by 4 mm) aluminum square tubing.

        - Floor Opening Application: Flange style cast aluminum fittings 5-1/2” x 2-3/4” x 1/4” (140 mm by 70 mm by 7 mm).

      - Self-closing gate: Aluminum (6005-T5) 1-1/4” (32 mm) schedule 40 pipe with 1-5/8” (42 mm) OD hinged on open side.

      - Hardware: Corrosion resistant hardware and fasteners is standard.

      - Finish:  Mill finish aluminum

  - FABRICATION

    - Completely fabricate aluminum guard rail system ready for installation before shipment to the site.

- EXECUTION

  - EXAMINATION

    - Do not begin installation until rough opening and structural support have been properly prepared.

    - If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

    - Examine materials upon arrival at site.  Notify the carrier and manufacturer of any damage.

  - INSTALLATION

    - Install in accordance with approved submittals.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION