4G Translator Machine

Selling points：

1、Artificial Intelligence product:  Intelligent speed recognition, Intelligent text translation, Intelligent text to speech conversion.

2、Accurate and fast translation；

3、Fast network connection：	4G/3G/2G+wifi，

4、Nano injection technology on product design；

5、Powerful and stable Qualcomm platform；

6、Easy to carry

# Introduction

- F 1 is based on the Qualcomm Snapdragon platform, which is a 4G LTE supported multi-languages translation products. It supports GSM/EDGE/TD-SCDMA/WCDMA/CDMA/EVDO/LTE which can be used world-widely.

## F1 Main SPECS

- Supported bands: see below specs.

- GSM/EDGE/TD-SCDMA/WCDMA/CDMA/EVDO/LTE

- 4GLTE

- WIFI

- WiFi hotspot / Mifi function

- Supports 16 languages multiple translations.

- 0.3S translation speed

- 97% accuracy (Chinese- English)

- IPS LCD

- Aluminium Alloy CNC+ Nano injection molding technology

- Big battery，2300MAh，standby time is 120hrs

- Low power consumption

- Customized bands

- New languages customization service

# Detail SPECS

- F1 detail SPECS is below：

| Main features | Description |
| --- | --- |
| Voltage | 3.4V～4.2V（recommend3.8V） |
| Working Bands | TD-LTE：Band 38/39/40/41 FDD-LTE：Band 1//3/5/8 WCDMA： Band 1/5/8 CDMA/EVDO：BC0 TD-SCDMA：Band 34/39 GSM/GPRS/EDGE：850/900/1800 |
|  | TDD | 3GPP R9 CAT4 Descending 150 Mbps，Ascending50 Mbps |
|  | FDD | 3GPP R9 CAT4Descending150 Mbps，Ascending 50 Mbps |
|  | WCDMA | DC-HSPA+ Descending 42 Mbps ，Ascending 5.76 Mbps |
|  | CDMA | CDMA2000 1X |
|  | EVDO | Descending 3.1 Mbps，Ascending1.8 Mbps |
|  | TD-SCDMA | Descending2.8 Mbps，Ascending2.2 Mbps |
|  | EDGE | Class 12，Descending236.8 kbps，Ascending118 kbps |
|  | GPRS | Class 10，Descending85.6 kbps，Ascending85.6 kbps |
|  | GSM | CSD 9.6 kbps |
| GPS | optional |
| Languages | Simple Chinese, English, Cantonese, Japanese, Korean, Thai, Arabic, Russian, Spanish, Vietnamese, French, Germany, Portuguese, Italian, Dutch, Greek |
| Infrared | optional |
| Working Temperature | Normal Temperature：-20℃～+60℃ Max. Temperature：-30℃～+75℃（1） Storage Temperature：-40℃～+85℃ |
| Working Humidity | 5%-95% |

Note：when it is30°C to –20°C and +60°C to +75°C, not all the RF Index is fit for 3GPP standards.

- External interface description

- F1：

| Interface | Description |
| --- | --- |
| Power | DC power input |
| USB | Micro USB |
| SIM CARD | Nano sim (Smallest one) |
| LCD | IPS TFT |
| MIC | 2x MIC |
| Speaker | Xbox |
| Earphone | 3.5MM |
| Keys | Power, V+ and V-, Menu, Repeat/Back, Select + and Select - button |