SECTION 11 33 00

RETRACTABLE STAIRS

- GENERAL

  - SECTION INCLUDES

    - Manual disappearing stairways.

  - REFERENCES

    - ANSI A14.9:  Safety Requirements for Ceiling Mounted Disappearing Climbing Systems.

  - SUBMITTALS

    - Submit under provisions of Section 01300.

    - Manufacturer's data sheets on each product to be used, including:

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

      - Installation methods.

    - Shop Drawings for Stairs:

      - Plan and section of stair installation.

      - Indicate rough opening dimensions for ceiling and/or roof openings.

  - DELIVERY, STORAGE, AND HANDLING

    - Store stairway until installation inside under cover in manufacturer's unopened packaging. If stored outside, under a tarp or suitable cover.

  - WARRANTY

    - Limited Warranty: One year against defective material and workmanship, covering parts only. Defective parts, as deemed by the manufacturer, will be replaced at no charge, freight excluded, upon inspection at manufacturer's plant.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: Precision Stairways, P. O. Box 2279; Morristown, TN 37816-2279; Tel: 423-586-2265; Fax: 423-586-2091; www.PrecisionStairways.com

    - Requests for substitutions will be considered in accordance with provisions of Section 01600.

  - MANUAL DISAPPEARING STAIRWAY.

    - Manual Disappearing Stairway.

      - Standard Model:  Super Simplex Disappearing Stairway as manufactured by Precision Stairways.  Stairs for ceiling heights 7’-0” – 12’-0”: Model 1000 (ceiling height in inches). Stairs for ceiling heights 12’-1” – 13’-6”: Model 2000 (ceiling height in inches).

    - Performance Standard:  Unit shall comply with ANSI A14.9, Commercial Type, for rough openings between 27 inches to 39 inches. Residential Type for rough openings between   22-1/2” and 27”.  Stairway capacity shall be rated at 500 lbs.

    - Accessories:

      - Steel pole to aid opening and closing stairways.

      - Stairs for ceiling heights 9’ -10” – 12’ -0” shall be equipped with a patented Precision Fold Assist to aid in folding and unfolding of sections.  Stairs for ceiling heights 12’ 1” – 13’6” shall be equipped with 2 Fold Assists.  Precision Fold-Assist is optional on stairways for ceiling heights of 9’ 9” and below.

      - Keyed lock for door (standard on fire-rated models, optional on non-fire-rated models).

    - Components:

      - Ceiling Opening

        - Ceiling height of 9’ 9” or less requires an opening of 30” x 54”

        - Ceiling heights from 9’ 10” – 12’ 0” require opening of 30” x 64”

        - Ceiling heights from 12’ 1” – 13’ 6” require opening of 22 ½” x 72”

      - Stairway Stringer: 6005-T5 Extruded aluminum channel 5” x 1” x 1/8”; tri-fold design; steel blade type hinges; adjustable feet with plastic Mar-guard.  Pitch shall be 63°.

      - Stairway Tread: 6005-T5 extruded aluminum channel 5 3/16 inches by 1 1/4 inches by 1/8 inch. Depth is 5 3/16 inches. Deeply serrated top surface. Riser Height: 9-1/2 inches. Clear Tread Width for Standard Width: 18 inches.

      - Railing: Aluminum bar handrail riveted to stringers, upper section only.

      - Frame:

        - If ceiling to floor (or roof deck) above is under 12”, frame shall be 1/8” steel formed channel, box.

        - When ceiling to floor (or roof deck) above is 12” or greater, the frame shall be 1/8” steel, 63° (with built-in steps) on the hinge end, 90° on the other end, custom depth to fill distance from ceiling to floor above.  This custom frame will require a longer opening in the floor above than is required at the ceiling level.

      - Door Panel

        - Standard (non-fire rated) door shall be constructed of 1/8 inch (3 mm) aluminum sheet attached to stairway frame with a steel piano hinge. Door overlaps bottom flange of frame. Eye bolt accommodates pole for opening and closing door.

        - On fire-rated models, the door panel shall be constructed of 20 gauge steel and have a 2 hour fire rating for use in fire-rated ceiling assemblies as issued by Warnock-Hersey or other appropriate independent testing/licensing agency.

      - Hardware:

        - Steel blade type hinge connecting stringer sections. Zinc plated and chromate sealed.

        - Steel operating arms, both sides. Zinc coat with clear trivalent chromate.

        - Double acting steel springs and cable, both sides.

        - Rivets rated at 1100 lb (499 kg) shear strength each.

        - Steel section alignment clips at stringer section joints.

        - Molded rubber guards at corners of aluminum door panel.

      - Finishes: Mill finish on aluminum stairway components. Prime coat on frame.

  - FABRICATION

    - Completely fabricate ladder ready for installation before shipment to the site.

- EXECUTION

  - EXAMINATION

    - Do not begin installation until rough opening and structural support have been properly prepared.

    - If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

    - Examine materials upon arrival at site.  Notify the carrier and manufacturer of any damage.

  - INSTALLATION

    - Install in accordance with manufacturer's instructions.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION