SECTION 11 33 00

RETRACTABLE STAIRS

- GENERAL

  - SECTION INCLUDES

    - Automatic disappearing stairways.

  - RELATED SECTIONS

    - Section 05 12 00 - Structural Steel Framing:  Roof structure and opening support.

    - Section 05 55 00 - Metal Stair Treads and Nosings:  Miscellaneous metal supports.

    - Section 06 10 00 - Rough Carpentry:  Roof framing and opening support.

    - Section 07 42 00 - Wall Panels:  Roof curb flashing.

  - REFERENCES

    - ANSI A14.9:  Safety Requirements for Ceiling Mounted Disappearing Climbing Systems.

  - SUBMITTALS

    - Submit under provisions of Section 01300.

    - Manufacturer's data sheets on each product to be used, including:

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

      - Installation methods.

    - Shop Drawings for Stairs:

      - Plan and section of stair installation.

      - Indicate rough opening dimensions for ceiling and/or roof openings.

  - DELIVERY, STORAGE, AND HANDLING

    - Store stairway until installation inside under cover in manufacturer's unopened packaging. If stored outside, under a tarp or suitable cover.

  - WARRANTY

    - Limited Warranty: One year against defective material and workmanship, covering parts only. Defective parts, as deemed by the manufacturer, will be replaced at no charge, freight excluded, upon inspection at manufacturer's plant.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: Precision Stairways, which is located at: P. O. Box 2279; Morristown, TN 37816-2279; Toll Free Tel: 800-225-7814; Tel: 423-586-2265; Fax: 423-586-2091; Web: www.PrecisionStairways.com

    - Requests for substitutions will be considered in accordance with provisions of Section 01600.

  - AUTOMATIC DISAPPEARING STAIRWAY.

    - Automatic Disappearing Stairway and Components: Stair, frame, stringers, treads, railing, motor and finishes.

      - Model:  Model S4*** (***=height in vertical inches) for stairs with ceiling heights of 8’-0” – 13’-6” (2438 mm – 4115 mm).  Automatic Super Simplex Disappearing Stairway as manufactured by Precision Stairways.

      - Capacity:  Unit shall support a 500 lb (227 kg) total load without failure.

      - Degree of Incline: 63 degrees.

      - Performance Standard:  Unit shall comply with ANSI A14.9; Commercial Type, for a rough opening of 30 inches (762 mm) and Residential Type, for a rough opening of 30 inches (762 mm).

    - Components:

      - Ceiling Opening:

        - Ceiling height of 9’-9” (2972 mm) or less requires an opening of 30 inches by 54 inches (762 mm by 1372 mm).

        - Ceiling heights from 9’-10” – 12’-0” (2997 mm by 3658 mm) require opening of 30 inches by 64 inches (762 mm by 1626 mm).

        - Ceiling heights from 12’-1” – 13’-6” (3683 mm – 4115 mm) require opening of 30 inches by 72 inches (762 mm by 1829 mm).

      - Stairway Stringer: 5 inch by 1 inch by 1/8 inch (127 mm by 25 mm by 3 mm) extruded 6005-T5 aluminum channel; tri-fold design; steel blade type hinges; adjustable feet with rubber rollers.

      - Stairway Treads: 5 3/16 inch by 1-1/4 inch by 1/8 inch (132 mm by 32 mm by 3 mm) extruded 6005-T5 aluminum channel. Depth is 5-3/16 inches (132 mm). Deeply serrated top surface. Riser Height: 9-1/2 inches (241 mm). Clear Tread Width for Standard Width: 16-1/2 inches (419 mm).

      - Railing: Aluminum tube, upper section only.

      - Frame:

        - If ceiling to floor (or roof deck) above is under 12 inches (305 mm), frame shall be 1/8 inch (3 mm) steel formed channel, box.

        - When ceiling to floor (or roof deck) above is 12 inches (305 mm) or greater, the frame shall be 1/8 inch (3 mm) steel, 63 degrees (with built-in steps) on the hinge end, 90 degrees on the other end, custom depth to fill distance from ceiling to floor above.  This custom frame will require a longer opening in the floor above than is required at the ceiling level.

        - When exit is to a roof deck, the frame must be 39 inches (991 mm) deep.

      - Door Panel:

        - Standard (non-fire rated) door shall be constructed of 1/8 inch (3 mm) aluminum sheet attached to stairway frame with a steel piano hinge. Door overlaps bottom flange of frame.

      - Hardware:

        - Steel blade type hinge connecting stringer sections. Zinc plated and chromate sealed.

        - Steel operating arms, both sides. Zinc coat with clear trivalent chromate.

        - Double acting steel springs and cable, both sides.

        - Rivets rated at 1,100 lb (499 kg) shear strength each.

        - Steel section alignment clips at stringer section joints.

        - Molded rubber guards at corners of aluminum door panel.

      - Motor: 110 volt.

      - Finishes: Mill finish on aluminum stairway components. Prime coat on frame.

    - Accessories:

      - Keyless Keypad Operation (Standard).

      - Push Button Operation (Standard – to open from above).

      - Battery Back-up (Standard).

      - Emergency Release Cable (Standard). Ensure the cable is accessible from ground floor.

  - FABRICATION

    - Completely fabricate stairway ready for installation before shipment to the site.

- EXECUTION

  - EXAMINATION

    - Do not begin installation until rough opening and structural support have been properly prepared.

    - If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

    - Examine materials upon arrival at site.  Notify the carrier and manufacturer of any damage.

  - INSTALLATION

    - Install in accordance with manufacturer's instructions and approved submittals.

    - A 110-volt power source is required to power motor.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION