EASY

Self Service Washing Bays

EASY 1

EASY 2

EASY 1

Self-service compact,  high-pressure hot water washer for 1 self service bay only, with chemical products (shampoo/wax) dosing pumps.

After the insertion of a coin or a token the operator may wash his vehicle through the selection of 5 washing phases.

The unit is encased in a stainless steel cabinet; doors are painted, pre-galvanized carbon steel.

## Washing phases

- Pre-wash – with detergent, hot softened water at high   pressure

- Brush/Foam - Washing with brush and foam (option)

- Wash – with cold water at high pressure

- Wax – with wax at medium pressure and with cold water

- Final rinse – with cold de-mineralized water at high pressure

*     Time of duration of the token is electronically set by    software.

## Main Components

- Hot-galvanised and painted single-bay technical cabinet with internal electrical heating with temperature control, equipped with holes for transport by lift and clamps to fix on the ground

- High pressure pump 100Bar 12l/minute, 140 Kw, mod. “INTERPUMP”

- 4-8 pole, 2,2 W motor/s, 100LA HP3 220/380 50 Hz motor. IP 55 cable shaft

- Electric dosing pumps (shampoo and wax)

- IP 55 electric system

- Frost protection device, wiping lance (to avoid ice through pipes)

- Inner independent frost protection device equipped with electrical resistor and control thermostat

- Containers for chemical products

- Electric panel with PLC for multifunction control

- Osmosis group with a production of 200l/h and a 100-litre container for the osmosis water with softener group (optional)

- Electric water heater 4,8 kW

- 360° rotating boom to support and bear high-pressure pipe and spray-gun

Machine command panel complete with:

- Token or Coin Acceptor

- Time/token display

- Lit program selection buttons

- Emergency stop button

- Lit network pilot light

- Lit “Out of service” pilot light

- Internal Token/coin collection container

Technical features

- Water supply pressure: 0,08÷0,25 Mpa (0,8÷2,5 bar)

- Mains water connection: 3/4 "

- Supply voltage: 400/230V ± 10%  50 Hz, 3/N/PE

- Installed electric power:  8 kW

- Absorbed current (400V): 12A

- Water consumption: 12 litres/min

- Dimensions in mm: 1245 x 650 x 2100

- Load-less weight: 300 Kg

Water treatment with softener and osmosis (option)

- Water softener resin type, ionic exchange

- Salt tank capacity: 20 Kg

- Water consumption: 200 lt/h

- Tank capacity: lt. 40

- Standard osmotic production: 210 lt/h at 1,4 MPa (14 bar)

EASY 2

Self-service compact,  high-pressure hot water washer for 2 self service bays, with chemical products (shampoo/wax) dosing pumps .

After the insertion of a coin or a token the operator may wash his vehicle through the selection of 5 washing phases.

The unit is encased in a stainless steel cabinet; doors are painted, pre-galvanized carbon steel.

## Washing phases

- Pre-wash – with detergent, hot softened water at high   pressure

- Brush/Foam - Washing with brush and foam (option)

- Wash – with cold water at high pressure

- Wax – with wax at medium pressure and with cold water

- Final rinse – with cold de-mineralized water at high pressure

*     Time of duration of the token is electronically set by    software.

## Main Components

- Hot-galvanised and painted single-bay technical cabinet with internal electrical heating with temperature control, equipped with holes for transport by lift and clamps to fix on the ground

- High pressure pump 100Bar 12l/minute, 140 Kw, mod. “INTERPUMP”

- 4-8 pole, 2,2 W motor/s, 100LA HP3 220/380 50 Hz motor. IP 55 cable shaft

- Electric dosing pumps (shampoo and wax)

- IP 55 electric system

- Frost protection device, wiping lance (to avoid ice through pipes)

- Inner independent frost protection device equipped with electrical resistor and control thermostat

- Containers for chemical products

- Electric panel with PLC for multifunction control

- Osmosis group with a production of 200l/h and a 100-litre container for the osmosis water with softener group (optional)

- Electric water heater 4,8 kW

- 360° rotating boom to support and bear high-pressure pipe and spray-gun

## Machine command panel complete with:

- Token or Coin Acceptor

- Time/token display

- Lit program selection buttons

- Emergency stop button

- Lit network pilot light

- Lit “Out of service” pilot light

- Internal Token/coin collection container

## Technical features

- Water supply pressure: 0,08÷0,25 Mpa (0,8÷2,5 bar)

- Mains water connection: 3/4 "

- Supply voltage: 400/230V ± 10%  50 Hz, 3/N/PE

- Installed electric power:  8 kW

- Absorbed current (400V): 12A

- Water consumption: 12 litres/min

- Dimensions in mm: 1245 x 650 x 2100

- Load-less weight: 300 Kg

## Water treatment with softener and osmosis (option)

- Water softener resin type, ionic exchange

- Salt tank capacity: 20 Kg

- Water consumption: 200 litri/h

- Tank capacity: lt. 40

- Standard osmotic production: 210 lt/h at 1,4 MPa (14 bar)