SECTION 11 33 00

RETRACTABLE STAIRS

- GENERAL

  - SECTION INCLUDES

    - Automatic electric disappearing stairways.

  - RELATED SECTIONS

    - Section 05 12 00 - Structural Steel Framing:  Roof structure and opening support.

    - Section 05 55 00 - Metal Stair Treads and Nosings:  Miscellaneous metal supports.

    - Section 06 10 00 - Rough Carpentry:  Roof framing and opening support.

    - Section 07 42 00 - Wall Panels:  Roof curb flashing.

  - REFERENCES

    - ANSI A14.9:  Safety Requirements for Ceiling Mounted Disappearing Climbing Systems.

  - SUBMITTALS

    - Submit under provisions of Section 01300.

    - Manufacturer's data sheets on each product to be used, including:

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

      - Installation methods.

    - Shop Drawings for Stairs:

      - Plan and section of stair installation.

      - Indicate rough opening dimensions for ceiling and/or roof openings.

  - DELIVERY, STORAGE, AND HANDLING

    - Store stairway until installation inside under cover in manufacturer's unopened packaging. If stored outside, under a tarp or suitable cover.

  - WARRANTY

    - Limited Warranty: One year against defective material and workmanship, covering parts only. Defective parts, as deemed by the manufacturer, will be replaced at no charge, freight excluded, upon inspection at manufacturer's plant.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: Precision Stairways, which is located at: P. O. Box 2279; Morristown, TN 37816-2279; Toll Free Tel: 800-225-7814; Tel: 423-586-2265; Fax: 423-586-2091; Web: www.PrecisionStairways.com

    - Requests for substitutions will be considered in accordance with provisions of Section 01600.

  - AUTOMATIC ELECTRIC DISAPPEARING STAIRWAY.

    - Automatic Electric Disappearing Stairway and Components:  Stair, rail, frame, door, drive unit, motor and controls/junction box, and finishes.

      - Model: Model AE*** (***=height in vertical inches) for stairs with ceiling heights of 7’-0” – 19’-3 3/4” (2438 mm – 4115 mm).  Automatic Electric Disappearing Stairway as manufactured by Precision Stairways.

      - Capacity: Unit shall support a 1000 lb (453 kg) total load without failure.

      - Degree of Incline: 52 degrees.

      - Performance Standard: Unit shall comply with ANSI A14.9; Commercial Type, for a rough opening of 30 inches (762 mm) and Residential Type, for a rough opening of 30 inches (762 mm).

    - Components:

      - Ceiling Opening:

        - Floor-to-floor height up to 14’-0” (4267 mm) requires an opening of 30 inches by 72 inches (762 mm by 1829 mm).

        - Floor-to-floor height greater than 14’-0” (4267 mm) requires an opening of 30 inches by 84 inches (762 mm by 2134 mm).

      - Stairway Stringer: 7 inches by 0.230 inch (178 mm by 5.8 mm) extruded 6005-T5 aluminum channel. Steel rollers at base of each stringer.

      - Stairway Tread: 6 inches by 20-3/16 inches by 0.225 inch (152 mm by 513 mm by 5.7 mm) extruded 6005-T5 aluminum channel.  Nonskid safety material at walking surface.  Riser Height: 9-1/2 inches (241 mm) maximum.  Clear Tread Width for Standard Width: 16-5/8 inches (422 mm).

      - Railing: Hand/guide rail 1-1/16 inches (27 mm) OD both sides, galvanized.

      - Frame: 1/8 inch (3 mm) steel formed channel. Height to suit total ceiling thickness.

      - Door Panel: 1/8 inch (3 mm) aluminum panel. Steel piano hinge.

      - Drive Unit: 1/3 horsepower (246 W), 115 volt instantly reversible motor direct-connected to a reduction gear drive, complete with contactors. Pre-wired control switches. Sealed ball bearing guides. Double 1/8 inch (3 mm) aircraft cable drive.

      - Finishes: Mill finish on aluminum stairway components. Prime coat on frame. Galvanized handrails.

    - Accessories:

      - Standard toggle wall mounted switch or key-operated switch (optional).

      - Battery backup power to open the stair in the event of a power failure (standard).

      - Warning buzzer (optional) sounds when stairway is in motion.

  - FABRICATION

    - Completely fabricate stair ready for installation before shipment to the site.

- EXECUTION

  - EXAMINATION

    - Do not begin installation until rough opening and structural support have been properly prepared.

    - If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

    - Examine materials upon arrival at site.  Notify the carrier and manufacturer of any damage.

  - INSTALLATION

    - Install in accordance with manufacturer's instructions and approved submittals.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION